## Slide 1
HACKATHON 2026
Smart Bus Arrival
Prediction System
Real-time bus tracking and arrival ETA using Arduino, GPS & GSM — bringing reliable transit information to every commuter.
Team • IoT × Embedded Systems × Cloud

## Slide 2
THE PROBLEM
Commuters wait without knowing when the bus will arrive.
⏱
Unpredictable Waits
Posted timetables rarely match reality due to traffic and route variability.
📍
No Live Visibility
Most city buses lack public real-time location feeds for commuters.
💸
Lost Productivity
Millions of hours wasted at bus stops every day across cities.
♿
Accessibility Gap
Elderly and differently-abled riders need predictable arrival times.

## Slide 3
OUR SOLUTION
An IoT device on every bus, predictions in every commuter's pocket.
How it works
1
Arduino + GPS captures bus location every few seconds.
2
GSM module transmits coordinates to our cloud server.
3
Server estimates ETA using distance, speed & traffic patterns.
4
Commuters view live bus position and arrival time on a web app.
Key Benefits
✓
Live ETA accurate to ~1 minute
✓
Low-cost hardware (< ₹1500 per bus)
✓
Works on 2G — coverage even in rural routes
✓
Scalable to entire city bus fleets
✓
Open data API for third-party apps

## Slide 4
ARCHITECTURE
End-to-end data flow from bus to commuter.
Bus Unit
Arduino UNO
NEO-6M GPS
SIM800L GSM
Cellular Network
GPRS / 2G
HTTP POST
Cloud Server
Node.js API
Database
ETA Engine
Commuter App
Web / Mobile
Live Map
Arrival ETA
Data flows every 5–10 seconds; ETAs recalculated continuously.

## Slide 5
HARDWARE
Affordable, off-the-shelf components.
Arduino UNO
Microcontroller — orchestrates GPS read and GSM transmit.
NEO-6M GPS Module
Acquires latitude, longitude, speed via NMEA over UART.
SIM800L GSM Module
Sends data to cloud over GPRS / HTTP.
1 kΩ & 4.7 kΩ Resistors
Voltage divider — steps Arduino 5V TX down to 3.3V for SIM800L.
1N4007 Diode
Drops Vin to a safe range for SIM800L power supply.
Breadboard & Jumper Wires
Prototyping connections between modules.

## Slide 6
CIRCUIT
Wiring overview — keep signal levels safe.
Connections
NEO-6M VCC
→ Arduino 3.3V
NEO-6M GND
→ Arduino GND
NEO-6M TX
→ Arduino D4 (SoftwareSerial RX)
NEO-6M RX
→ Arduino D3 (SoftwareSerial TX)
SIM800L VCC
→ 4V supply via 1N4007 diode from 5V
SIM800L GND
→ Arduino GND
SIM800L RX
→ Voltage divider (1k / 4.7k) from Arduino D8
SIM800L TX
→ Arduino D7
Why the divider?
Arduino's TX is 5V logic, but SIM800L expects 3.3V on RX. A 1 kΩ + 4.7 kΩ voltage divider safely reduces the level and prevents damage.
Why the diode?
SIM800L runs at 3.4–4.4V. A 1N4007 in series drops ~0.7V from 5V, giving a safe ~4.3V to the module.

## Slide 7
SOFTWARE STACK
From firmware to web dashboard.
Firmware
Arduino IDE
TinyGPS++ parses NMEA from NEO-6M. SoftwareSerial talks to SIM800L using AT commands to open a TCP / HTTP session and POST coordinates.
Backend
VS Code · Node.js
Express REST API ingests GPS pings, stores them in a time-series database, and runs the ETA prediction service for each bus stop.
Frontend
VS Code · React
Live map (Leaflet) shows every bus in real time. Riders pick a stop and see the next 3 arrivals with predicted ETAs.

## Slide 8
ETA ALGORITHM
Predicting arrival time with simple but effective math.
Core formula
ETA = Σ(segmentDistance / avgSpeed)
+ historical traffic delay
Distance is computed along the route polyline (not straight line). Average speed blends the bus's recent speed with the route's historical pace at this hour.
Pipeline
1.
Snap GPS point to nearest route segment.
2.
Compute remaining distance to target stop.
3.
Estimate avg speed (recent + historical).
4.
Add traffic/dwell buffer per time slot.
5.
Publish ETA via WebSocket every 5 s.

## Slide 9
FEATURES
What riders and operators actually get.
🗺
Live Map
Every bus as a moving pin, updated every 5 seconds.
⏰
Smart ETAs
Next 3 buses at the chosen stop, refreshed continuously.
🔔
Smart Alerts
Notify rider when bus is N minutes away.
📊
Operator Dashboard
Fleet health, route punctuality, bunching alerts.
🌐
Open API
Public read API for third-party apps and signage.
♿
Accessibility
High-contrast UI, voice readouts, large fonts.

## Slide 10
IMPACT & ROADMAP
Impact today, roadmap for tomorrow.
~₹1,500
Cost per bus unit
< 1 min
ETA accuracy target
5 sec
Update frequency
2G+
Network coverage
Roadmap
Phase 1
Pilot on 1 route — 5 buses, live map + ETA.
Phase 2
City-wide rollout, mobile app, SMS alerts for feature-phone users.
Phase 3
ML-based ETA (LSTM on historical traffic), payment & ticketing integration.

## Slide 11
Thank you.
Questions? Let's build smarter cities together.
Smart Bus Arrival Prediction System · Hackathon 2026